## Slide 1: Color & Graphics
The complete display system is:
  Model
  Frame Buffer
  Screen
  Eye
  Brain

## Slide 2: Color & Vision
We'll talk about:
  Light
  Visions
  Psychophysics, Colorimetry
  Color
    Perceptually based models
    Hardware models

## Slide 3: Light
Vision = perception of electromagnetic energy
Very small portion of EM spectrum is visible
More next class

## Slide 4: Vision: The Eye
A dynamic, biological camera!
  a lens
  a focal length
  an equivalent of film
The lens must focus directly on the retina for perfect vision
Retina
Lens

## Slide 5: Vision: The Retina
The eye's "film"
Covered with cells sensitive to light
  turn light into electrochemical impulses
Two types of cells
  rods
  cones

## Slide 6: Vision: Rods
400
700
Sensitive to most wavelengths (brightness)
About 120 million in eye
Most outside of fovea (center of retina)
Used for low light vision
Absorption function:

## Slide 7: Vision: Cones
Three kinds
  R sensitive to long wavelengths (L in book)
  G to middle (M in book)
  B to short (S in book)
About 8 million in eye
Highly concentrated in fovea
  B cones more evenly distributed than others
Used for high detail color vision

## Slide 8: Vision: Cones
The absorption functions of the cones are:

## Slide 9: Psychophysics
Spectral Energy Distribution
  measure intensity of light at unit wavelength intervals of electromagnetic spectrum from ~400 nm to ~700 nm

## Slide 10: Psychophysics
Dominant Wavelength  hue
Excitation Purity  saturation
Luminance  intensity
  Lightness: luminance from a reflecting object
  Brightness: luminance from a light source
To mix colors
  mix power distributions!

## Slide 11: Color Mixing: Additive
Luminous objects emit s.e.d.
Linearly add s.e.d.’s
Primaries: red green blue
Complements: cyan magenta yellow
e.g. Monitors, lights

## Slide 12: Color Mixing: Subtractive
Reflective objects absorb (or filter) light
Can’t subtract s.e.d.’s
  Filters: transmission functions
  Pigment: suspension, scattering of light
Primaries: cyan magenta yellow
Complements: red green blue
E.g., ink, film, paint, dye

## Slide 13: Colorimetry
Based on matching colors using additive color mixing
Tristimulous Values
Metamers
  Different s.e.d.’s that appear the same
  Same tristimulous values

## Slide 14: Colorimetric Color Models
Generated color match functions
  match each wavelength, multiple people
  some colors require negative red!
CIE produced two device independent models:
  1931: Measured on 10 subjects (!) on samples subtending 2 (!) degrees of the field of view
  1964: Measured on larger number of subjects subtending 10 degrees of field of view

## Slide 15: Color Match Functions

## Slide 16: CIE 1931 Imaginary Primaries
Defines three new primary “colors”
  X, Y and Z
  Mixtures positive valued
  Y’s fcn corresponds to luminance-efficiency function
To define a color
  weights x,y,z for the X,Y,Z primaries (e.g. color = xX + yY + zZ)

## Slide 17: CIE 1931 Chromaticity
X, Y and Z form a three dimensional color volume
  Y is luminance, others aren’t intuitive
Factor luminance by normalizing x+y+z = 1
Chromaticity values:
  x’ = x/(x+y+z)
  y’ = y/(x+y+z)
  z’ = 1 - x’ - y’

## Slide 18: CIE 1931 Chromaticity Diagram
Chromaticity diagram
  Plot of x’ vs. y’
Additive color mixing
  linear interpolation
Color gamuts
  range of possible colors for a device
  convex hull of primary colors
C = standard illuminant,
approximates sunlight, near 4K white
C
HDTV (ITU-R BT.709) and sRGB

## Slide 19: CIE 1931 Chromaticity Diagram
A
H
H’
Dominant Wavelength/Hue:
  inscribe line from C through color (A) to edge of diagram (H)
Saturation
  distance C-A distance C-H
Complements
  inscribe line through C to the edge of the diagram (H’)
What if edge is bottom?

## Slide 20: Hardware Models: RGB (Additive Color)
Hard to achieve intuitive effects:
Hue is defined by the one or two largest parameters
Saturation controlled by varying the collective minumum value of R, G and B
Luminance controlled by varying magnitudes while keeping ratios constant
(red, green, blue)
Parameters vary between 0 and 1

## Slide 21: Hardware Models: CMY, CMYK (Subtractive Color)
K = min (C,M,Y)
subtract K from each
(cyan, magenta, yellow, +blacK)
All parameters vary between 0 and 1
M
Y
C
black

## Slide 22: Intuitive Hardware Models: HSV
Simple xform of RGB
What do hexagonal and triangle cross sections look like?
(hue, saturation, value)
  value roughly luminance
  hue: (0...360), saturation/value: (0...1)

## Slide 23: Intuitive Hardware Models: HLS
saturated colors at l=0.5
tints above, shades below
What do hexagonal and triangle cross sections look like?
(hue, lightness, saturation)
  lightness roughly luminance
  hue: (0...360), saturation/value: (0...1)

## Slide 24: Problem: V/L != Luminance
Fully saturated colors (same v/l) have far different Y values in XYZ (Sun 17” monitor, 1991):
Colour RGB XYZ Chromaticity
White 1 1 1 0.951 1.000 1.088 0.313 0.329
Red 1 0 0 0.589 0.290 0.000 0.670 0.330
Green 0 1 0 0.179 0.605 0.068 0.210 0.710
Blue 0 0 1 0.183 0.105 1.020 0.140 0.080
Cyan 0 1 1 0.362 0.710 1.088 0.168 0.329
Magenta 1 0 1 0.772 0.395 1.020 0.363 0.181
Yellow 1 1 0 0.768 0.895 0.068 0.444 0.517

## Slide 25: Problem: None of these models are perceptually uniform
Perceived distance between two colors not proportional to linear distance
Uniform Color Spaces
  Non-linear deformations
  OSA Uniform Color Space (limited range)
  CIELUV
  CIELAB

## Slide 26: Issue: Device-independent color
Must use CIEXYZ
  ie. Apple Colorsync
RGB = (0.3,0.2,0.55) tells you what computer generates, not what the monitor will display!
  Depends on phosphors, room lighting, monitor adjustment
Moving between devices (and media)
  Go through XYZ
  Must know properties of devices