## Slide 1: 4 – Hardware, raster displays, color

## Slide 2: Basic Definitions
Raster: A rectangular array of points or dots.
Pixel: One dot or picture element of the raster
Scan Line: A row of pixels

## Slide 3: Example Raster Graphics Architecture
Display
processor
memory
Frame
buffer
Video
controller
Monitor
System
memory
CPU
Peripheral
devices
System bus
GPU/Display
processor
Raster system architecture with a display processor.
(originally from Computer Graphics: Principles and Practice.)

## Slide 4: Displays and Cameras
Book covers LED, LCD, ink-jet, dye sub, cameras and scanners
Bayer mosaic

## Slide 5: CRT Monitor
Electron Guns
Red Input
Green
Input
Blue Input
Deflection
Yoke
Shadow Mask
Red, Blue,
and Green
Phosphor Dots
CRT

## Slide 6: Electron Gun
Stream of electrons directed to front
  Num electrons controls brightness
Phosphor, glows briefly
Gaussian distribution of electrons, light

## Slide 7: Color CRT
RGB electron guns
Screen coated with phosphor pattern
Fluorescence
Phosphorescence
Persistence

## Slide 8: Shadow Mask
Phosphors arranged in triads
Each triad has one R/G/B phosphor dot
Typically 2.3 to 2.5 triads per pixel
Shadow mask has one small hole for each phosphor triad
SHADOW MASK
Red
Green
Blue
Convergence
Point
Phosphor Dot
Screen

## Slide 9: Scanning An Image to a Display
Frame: image to be scanned on CRT/LCD
Frame must be “refreshed” to eliminate flicker in the image.
Critical Fusion Frequency
  Typically 60 times/sec for raster displays
  Varies with intensity, individuals, phosphor persistence, lighting, …

## Slide 10: Interlaced Scanning
Assume can only scan 30 times/sec
To reduce flicker, divide frame into two “fields” (odd and even lines)

## Slide 11: Scanning
VERTICAL SYNC PULSE — Signals the start of the next field.
VERTICAL RETRACE — Time needed to get from the bottom of the current field to the top of the next field.
HORIZONTAL SYNC PULSE — Signals the start of the new scan line.
HORIZONTAL RETRACE — Time needed to get from the end of the current scan line to the start of the next scan line.

## Slide 12: Resolution and Addressability
(Everybody, incorrectly, uses resolution when they mean addressability.)
Resolution is a measure of the width of a single line drawn on the CRT screen (1/spotsize). Usually stated as the number of just merged lines per inch or centimeter.
Addressability is a measure of the spacing between the centers of those lines.
Resolution = Addressability
Resolution < Addressability
Smooths out the "jaggies" but the overlap will cause filled areas to be brighter than lines, and lines to be brighter than single pixels.

## Slide 13: Frame Buffers
2D array
  each (x,y) location = a pixel
Bit Planes, Bit Depth
  number of bits in a pixel
Typical frame buffers:
  640 x 480 x 8
  1280 x 1024 x 8
  1280 x 1024 x 24

## Slide 14: True Color Display 24 bitplanes, 8 bits R/G/B
Green
Red
Blue
N
N
N
2^24 = 16,777,216

## Slide 15: Color Map Look-Up Tables
LUT Video look-up table organization. A pixel with value 67
(binary 01000011) is displayed on the screen with the red electron
gun at 9/15 of maximum, green at 10/15, and blue at 1/15. This look-up
table is shown with 12 bits per entry. Up to 24 bits per entry are
common.
0
1
0
0
0
0
1
1
67
100110100001
0
67
255
1001
1010
0001
R
G
B
RED
GREEN
BLUE
Pixel displayed
at x', y'
Pixel in
bit map
at x', y'
0
x
0
y
x
max
max
y
Bit map
Look-up table
Display

## Slide 16: Camera
Aperture
Exposure
Images from https://en.wikipedia.org/wiki/Aperture

## Slide 17: Camera Focal Length
field of view = 2 atan (sensorsize / (2f))
http://www.dpreview.com/glossary/optical/focal-length

## Slide 18: Aperture, Depth of Field, and Bokeh
"Josefina with Bokeh" by carlosluis - http://www.flickr.com/photos/paseodelsur/51805888/.
"Christmas Tree Lights Bokeh" by Rushilf - Own work